## Slide 1
UART (Universal Asynchronous Receiver Transmitter Communication
Embedded SEED
Understanding UART Communication Protocol and its implementation on STM32L452RE Controller

## Slide 2
STM32 Cube IDE Configuration
Lab Name: A Hardware Communication Protocol Understanding Universal Asynchronous Receiver/Transmitter
Problem Statement: To Understand UART Communication Protocol and Implement the UART Transmission and Reception on STM32L452RE Controller
Objective: The Objecitve of this Experiment is to Help understand UART Communication, its Features and Handle Serial Terminal Software like Docklight.
Output: At the end of this experiment the students will be successfully able to implement UART Communication Protocol on STM32 Mico-controller.

## Slide 3
HARDWARE REQUIREMENTS
USB to TTL
2. Jumper Cables (Female to Female)

## Slide 4
UART, or universal asynchronous receiver-transmitter, is one of the most used device-to-device communication protocols.
Communication protocol plays a big role in organizing communication between devices.
Embedded systems, microcontrollers, and computers mostly use UART as a form of device-to-device hardware communication protocol

## Slide 5
The two signals of each UART device are named:
Transmitter (Tx)
Receiver (Rx)
The main purpose of a transmitter and receiver line for each device is to transmit and receive serial data intended for serial communication.
Parameters | Value
Speed | 9600, 19200, 384200, 57600, 115200, 230400, 460800, 921600, 1000000, 1500000
Methods of Transmission | Asynchronous
Min No of Masters | 1
Max No of Slaves | 1

## Slide 6
Data Transmission
In UART, the mode of transmission is in the form of a packet. The piece that connects the transmitter and receiver includes the creation of serial packets and controls those physical hardware lines. A packet consists of a start bit, data frame, a parity bit, and stop bits.

## Slide 7
Steps in UART Transmission and Reception
Step 1 - The transmitting UART receives data in parallel from the data bus ( From Micro-controller)
Step 2 -
The transmitting UART adds the start bit, parity bit, and the stop bit(s) to the data frame.
Step 3 - The entire packet is sent serially starting from start bit to stop bit from the transmitting UART to the receiving UART. The receiving UART samples the data line at the preconfigured baud rate.

## Slide 8
Step 4 - The receiving UART discards the start bit, parity bit, and stop bit from the data frame..
Step 5 - The receiving UART converts the serial data back into parallel and transfers it to the data bus on the receiving end.

## Slide 9
HARDWARE CONNECTIONS
GND
STM32L452RE µC
PC4 (UART TX
TO PC / LAPTOP

## Slide 10
Steps in Configuring STM32 UART Communication Protocol
STEP 1 – Open Cube IDE and Create a new Project
STEP 2 – Configure SYS as Serial Wire and RCC as Crystal Ceramic Resonator

## Slide 11
STEP 3 – Configure the Clock Source as 80 MHz and Select the Frequency as Input High Frequency (HIS) as Shown in the Figure

## Slide 12
STEP 4 – Click on Connectivity Option. Under Connectivity Select USART3.
STEP 5 – Click On Mode and Select Asynchronous. Keep the Settings as shown in the Figure.

## Slide 13
STEP 6 – In the main.c file write the code for UART Transmission and Build and if no errors are present run the Code.

## Slide 14
Step 2 – Once Docklight Website Opens, Select Download Docklight Option as shown in the figure
Steps to Install Dock-light Software
Step 1 – Open Google and Type Download Docklight for Windows. Click on the following link.

## Slide 15
Step 3 – Once Docklight Software is Downloaded, Install the Software. Click Run as Administrator.

## Slide 16
Step 4 – Setup Docklight. Click Next
Step 4 – Setup
Read Agreement and Click Next

## Slide 17
Specify Folder for Installation. Keep the Default Folder and Click Next
Click Next

## Slide 18
Check on Create Desktop icon and Click Next
Install the Application

## Slide 19
Once Installed, Open Docklight, And click OK when following Message Shows. Double Click on COM1.

## Slide 20
Select the desired COM Port and Select the Baud Rate to 115200 BPS

## Slide 21
Click on Run Button